## Slide 1
Performance Analysis of Parameterizable
HQC Hardware Architecture
Nishant Pandey, Sanjay Deshpande, Dixit Dutt Bohra, Debapriya Basu Roy, Dip Sankar Banerjee, and Jakub Szefer

## Slide 2: Quantum Threat and Post-Quantum Cryptography
Public-key cryptography
  Shor’s algorithm can potentially break existing pre-quantum public-key cryptosystems (e.g., RSA)
Post-Quantum Cryptography to the rescue!
  Algorithms run on classical computers
Post-Quantum Cryptography standardization efforts are in progress around the world

## Slide 3: NIST Post-Quantum Cryptography Standardization
26
Round 2
Submitted candidates belong to two categories
  PQ-KEM: Post-Quantum Key Encapsulation Mechanism
  PQ-DSS: Post-Quantum Digital Signature Scheme
Evaluation Criteria
  Security
  Hardware and Software implementation efficiency and security
  Cost (key size, signature size, etc.)
2016
Call for proposals
Round 1
2017
2018
2019
2020
2021
2022
2023
2024
2025
Round 2
Round 3
1 PQ-KEM (Kyber), 3 PQ-DSS selected
4 PQ-KEM for further evaluation
Concluded
1 PQ-KEM
(Hamming Quasi-Cyclic)
candidate selected
Call for proposals
Additional PQ-DSS
Round 1
69
8
40
14
ongoing
1
ML-KEM standard
published
2026
Round 3
9

## Slide 4: Secure and Efficient Implementations of Cryptographic Algorithms
Target platforms:
  CPU
  Microcontrollers
  Field-Programmable Gate Array (FPGA) : Artix 7
  Application Specific Integrated Circuit (ASIC)

## Slide 5
Hamming Quasi-Cyclic
(HQC)

## Slide 6: Key Encapsulation Mechanism
(APK, ASK)←KeyGen(seed)
K’←Decap(ASK, C)
(K, C)←Encap(APK)
Alice’s
Public Key
Alice’s
Secret Key
APK
C
Encapsulated Key
Ciphertext
Decapsulated Key
Secure Channel
Symmetric Encryption

## Slide 7: Hamming Quasi Cyclic (HQC)
Parameter Set | Security | n | w | ¦ek¦ | ¦dk¦ | ¦ct¦
HQC-1 | 128 | 17,669 | 66 | 2,241B | 2,321B | 4,433B
HQC-3 | 192 | 35,851 | 100 | 4,514B | 4,602B | 8,978B
HQC-5 | 256 | 57,637 | 131 | 7,237B | 7,333B | 14,421B
A code-based KEM scheme based on the syndrome decoding hard problem.
Construction is based on concatenated codes:
  Shortened Reed Solomon code and
  Duplicated Reed-Muller code
n - degree of the polynomial
w - weight
keypair – (ek,dk)
ct - ciphertext

## Slide 8: Key Generation
Sample
Sample
Fixed
Weight
Vectors
Polynomial Multiplication
(h.y)
Polynomial Addition
x+h.y
h
x
y
s
public key seed
(SeedPKE.ek)
secret key seed
(SeedPKE.dk)
ekPKE = (h,s)
dkPKE = (x,y)

## Slide 9: HQC Primitives
Performance Bottleneck.
95-96% across different parameter sets
Key Generation
Encapsulation
Decapsulation

## Slide 10: Limitations of Existing Work
Existing work includes
  Full hardware [SAC’23, HOST’24]
  High-level synthesis [CBCrypto’23]
  Hardware-Software codesign [WF-IoT’23]
Chart: Operations per second
| HW/SW [WF-IoT'23] | HLS [CBCrypto'23] | HW [HOST'24]
decap. | 180 | 779 | 7813
encap. | 763 | 1644 | 12195
keygen. | 1786 | 3700 | 33333
Higher is better
HQC-1

## Slide 11: FPGA Implementation Performance and Evaluation Metrics
Time
Area
Area-Time product
  Time * {max{LUT/4, FF/8} + 128 ∗ BRAM + 100 ∗ DSP}
Input/Output
connections
Configurable logic block
(CLB)
Memory Blocks
(Block RAM)
DSP Blocks
Typical FPGA
Architecture
LUT
FF
MUX
a
b
clk
out

## Slide 12: Limitations of Existing Work
Existing work includes
  Full hardware [SAC’23, HOST’24]
  Hardware-Software codesign [CBCrypto’23]
  High-level synthesis [WF-IoT’23]
Previous implementations lack
  Tweakable performance parameters
  Support for new parameter sets
Chart: Operations per second
| HW/SW [WF-IoT'23] | HLS [CBCrypto'23] | HW [HOST'24]
decap. | 180 | 779 | 7813
encap. | 763 | 1644 | 12195
keygen. | 1786 | 3700 | 33333
Chart: Time – Area Product
| HW/SW [WF-IoT'23] | HLS [CBCrypto'23] | HW [HOST'24]
Time x Area | 17736 | 14474 | 3105
Higher is better
Lower is better
HQC-1

## Slide 13
Performance Bottleneck
Fixed-Weight Vector

## Slide 14: Fixed Weight Vector – Constant Weight Word Method
PRNG
index[i] = i+ prng_bits %(N-i)
i+1
Weight
== w?
Duplicate
Check?
Constant time method proposed by Sendrier [SEN21].
pos = index[i]
pos = i
{0,1,0,0,0,1,0,0,…,0}
set the position
value to ‘1’
start
done
[SAC’23]
Technique: Brute-force pairwise comparison.
Complexity O(w^2)
[Our]
Technique: One-pass traversal technique – trades off space for speed
Complexity: O(w)

## Slide 15: Fixed Weight Vector Generation - Evaluation
Chart: Timing comparison
| Our | SAC'23
HQC-1 | 2.4 | 15.96
HQC-3 | 3.41 | 36.27
HQC-5 | 4.71 | 61.12
Chart: Area-Time Product comparison
| Our | SAC'23
HQC-1 | 4 | 6
HQC-3 | 5 | 13
HQC-5 | 7 | 22
Lower is better
Lower is better
HQC-1
HQC-1

## Slide 16
Performance Bottleneck
Polynomial Multiplication

## Slide 17: Polynomial Multiplication
B(x)=b0+b1x+b2x2+⋯+bnxn
A(x)=a0​+a1​x+a2​x2+⋯+an​xn
Chart: Complexity of polynomial multiplication
| HQC-1 | HQC-3 | HQC-5
Schoolbook Method | 312 | 1285 | 3322
Karatsuba | 5.3 | 16.5 | 35.1
Toom-Cook | 1.6 | 4.7 | 9.4
Schoolbook = O(n2)
Karatsuba = O(n1.585)
Toom-Cook = O(n1.465)
Parameter Set | n | w
HQC-1 | 17,669 | 66
HQC-3 | 35,851 | 100
HQC-5 | 57,637 | 131
A & B are polynomials in F2

## Slide 18: Polynomial Multiplication involving Sparse Polynomials
B(x)=0+b1x+0+⋯+bmxm
A(x)=a0​+a1​x+a2​x2+⋯+an​xn
Chart: Complexity of polynomial multiplication
| HQC-1 | HQC-3 | HQC-5
Karatsuba | 5.3 | 16.5 | 35.1
Toom-Cook | 1.6 | 4.7 | 9.4
Sparse Poly Mult | 1.1 | 3.5 | 7.5
Karatsuba = O(n1.585)
Toom-Cook = O(n1.465)
Sparse poly mult = O(n.w)
Parameter Set | n | w
HQC-1 | 17,669 | 66
HQC-3 | 35,851 | 100
HQC-5 | 57,637 | 131
A & B are polynomials in F2

## Slide 19: Sparse F2 Polynomial Multiplication with Interleaved Reduction
Variable
Shifter/ Rotation
n
n
2n
n
n
n
Non-zero bit position from Sparse Input
Non-Sparse
Polynomial Input
Output Polynomial
n
Conceptual Block Diagram
Sparse
Multiplication
Interleaved
Reduction
Field polynomial: Xn-1: allows folding and adding the polynomial for reduction
The multiplication and the modular reduction is interleaved.
Addition is an XOR because all polynomials are in F2.
Indices of non-zero elements are used to shift non-sparse polynomial to imitate the multiplication.
Reduction in area
Reduction in memory utilization

## Slide 20: Sparse F2 Polynomial Multiplication Hardware Design
Hardware design of sparse polynomial multiplication module
W: Performance parameter [SAC’23]
Shifter
Block
RAM
Chart: Area-Time product comparison
| Our | [SAC'23]
W=1024 | 56 | 588
W=512 | 75 | 404
W=256 | 143 | 336
W=128 | 269 | 212
Lower is better
HQC-1
Chart: Timing comparison
| Our | [SAC'23]
W=1024 | 0.037887 | 0.0526
W=512 | 0.06656 | 0.085218
W=256 | 0.13433 | 0.14908
W=128 | 0.2755 | 0.24276
Lower is better
HQC-1

## Slide 21
Key Generation, Encapsulation,
and Decapsulation

## Slide 22: Joint Design – Sweep
Chart: Time – Area Product
| W=128 | W=256 | W=512 | W=1024
Time x Area | 2763 | 2139 | 1997 | 2354
Chart: Operations per second
| W=128 | W=256 | W=512 | W=1024
decap. | 5354.8387 | 7904.7619 | 10125 | 12384.6154
encap. | 10375 | 15090.9091 | 20250 | 23000
keygen. | 13833.3333 | 23714.2857 | 32400 | 40250
Joint Design – combines Keygen, Encap, and Decap into one.
Shared module among different primitives.
  SHAKE256
  Polynomial Multiplication
  Encapsulation
  Polynomial Addition
W – performance parameter
Time-Area product
  Time * max{LUT/4 + 128 ∗ BRAM + 100 ∗ DSP, FF/8}
Higher is better
HQC-1
FPGA: AMD Artix 7
Lower is better

## Slide 23: Joint Design – Comparison with other HQC Hardware Designs
Chart: Time – Area Product
| HW/SW [WF-IoT'23] | HLS [CBCrypto'23] | HW [HOST'24] | Our
Time x Area | 17736 | 14474 | 3105 | 2354
Chart: Operations per second
| HW/SW [WF-IoT'23] | HLS [CBCrypto'23] | HW [HOST'24] | Our
decap. | 180 | 779 | 7813 | 12385
encap. | 763 | 1644 | 12195 | 23000
keygen. | 1786 | 3700 | 33333 | 40250
Higher is better
HQC-1
FPGA: AMD Artix 7
Lower is better
Only Poly. Mult. on FPGA
Full design on FPGA

## Slide 24: Summary
Key Generation
Encapsulation
Decapsulation
Design and evaluation of performance critical aspects of HQC implementation
When compared to state-of-the-art we demonstrated:
  20% improvement in Key Generation time
  80% improvement in Encapsulation time
  60% improvement in Decapsulation time
  33% improvement in the Time–Area product

## Slide 25
Thank you!
https://sanjaydeshpande.phd/
Performance Analysis of Parameterizable
HQC Hardware Architecture

## Slide 26
Backup
Slides

## Slide 27: What about NTT/FFT type multiplication for HQC?
Cannot directly apply NTT (Number Theoretic Transform) to binary field polynomial multiplication
  Requires a finite field with special roots of unity
Chen et. al [CCK21] proposed using Frobenius Additive FFTs (FAFFT).
  Implemented in hardware by Ras et. al [RLC+25]

## Slide 28: Frobenius Additive FFT (FAFFT)
Convert to new polynomial basis – Cantor Basis.
FFT Encode and FFT Decode are used to reduce the number of evaluations.
a
b
BC
BC
FFT
Encode
FFT
Encode
x
BC
FFT
Decode
c
F2 -> F2
m
F2 -> F2
m
FFT
IFFT

## Slide 29: Performance FAFFT vs Sparse Multiplication
Chart: Time comparison
| FAFFT Mult. [RLC+25] | Sparse Mult. (our)
BC - begin | 109940
FF Encode | 553766
FFT | 11520
Multiplication | 1102 | 36698
IFFT | 5760
FFT Decode | 764880
BC - end | 98576
Other | 332353
1,877,897
Freq
(125 MHz)
(288 MHz)
Taking advantage of sparsity doesn’t lead to non-constant time behavior on hardware.
  Weight of the sparse polynomial is fixed.
HQC128

## Slide 30: Comparison HQC vs CRYSTALS-Kyber
Scheme | Sizes (Bytes) |  | 
 | ek | dk | ct
HQC128 | 2,241 | 4,602 | 7,333
Kyber512 | 800 | 1,632 | 768
Scheme | Device | Keygen | Encap | Decap | Freq. (MHz) | Area |  |  | 
 |  | Kcycles |  |  |  | KLUT | KFF | DSP | BRAM
HQC-1 [our] | Artix-7 | 5 | 8 | 16 | 162 | 26 | 27 | 8 | 32.5
Kyber-512 [BMG+21] | Artix-7 | 2 | 3 | 5 | 220 | 10 | 9 | 4 | 4.5
Scheme | Device | Keygen | Encap | Decap | Freq. (MHz)
 |  | Kcycles |  |  | 
HQC-1 [GAA+25] | Intel Core i7-11850H | 76 | 150 | 353 | 2,500
Kyber-512 [ABD+21] | Intel Core i7-4770K | 34 | 45 | 35 | 3,492
Key Sizes
CPU Cycle Comparison
FPGA Implementation Comparison

## Slide 31: Syndrome Decoding Problem
h, 𝑥, 𝑦 are ‘n’ degree polynomials
Setup:
  h – sampled from a pseudo-random number generator (PRNG)
  𝑥, 𝑦 – non-zero location of the sparse polynomial sampled from a PRNG
x
+
=
𝑥
𝑦
h
pseudorandom polynomial
Sparse fixed-weight polynomial
S = 𝑥 + h .𝑦
Sparse fixed-weight polynomial
h and S are public
𝑥 and 𝑦 are secret
Given h and S, finding 𝑥 and 𝑦 is hard!